## Slide 1
Introduction to image processing and analysis with ImageJ / Fiji. Part 2 ImageJ / Fiji – The basics
Dale Moulding
UCL Institute of Child Health Imaging Facility

## Slide 2
Tool Bar
Menu Bar
Status Bar
Macro
toolset
switcher
Double left click: opens the option window
Right click: selects a different tool
ImageJ/Fiji interface
Remember ! All operations are performed on the active window i.e. the frontmost image with the highlighted title bar.
Progress Bar

## Slide 3
File>Open
Drag and Drop (files/folders)
File>Import>Image Sequence … (if you have a folder full of files that make a movie or 3D stack)
How to open your files…

## Slide 4
File>Import>Image Sequence
Opens a series of images in a folder as a stack. The images must all be the same size and type.
1- Select folder and one file
2- Specify options
Example: zebrafish

## Slide 5
Works with single files,
multiple files or folder
Drag and drop
Try it with the Zebrafish folder

## Slide 6
File>Save (as Tiff the active window)
      Caution : If the original file is already a Tiff file, it will be replaced by the new file !
File>Save as…
      Tiff (8-bit, 16-bit, 32-bit float and 24-bit RGB)
      ZIP : as tiff in a compressed ZIP archive
      Image sequence : every slice of a stack (Z or time) save as individual tiff file.
      Others formats
      DO NOT USE JPEG LOSSY COMPRESSION
Saving data

## Slide 7
File Menu
All self explanatory
but wait a minute…
Revert (re-opens last saved version)
Fix Funny Filenames!?!
Make Screencast:
records a movie of the screen as an .ogv file
You can change it to an .mp4 file in ‘Handbrake’,
where you can also crop and clip the movie.

## Slide 8: Edit Menu
Not always available
Copy to the internal clipboard
the content of the internal clipboard (Can check by File > New > System Cilpboard – Ctrl + Shift + V)
clear the selection and replace by background colour
clear outside the selection and replace by background colour
fill the selection with foreground color
outlines the selection (I prefer ROI manager for drawing)
creates a “negative image”

## Slide 9
Edit / Options >
Saving options (jpeg quality, results output)
Change corner sizes
Very useful…
Details later
Change foreground & background colours
Startup macros
Use CTRL key
for shortcuts

## Slide 10
Edit>Selection Menu
Transfer selection between images
Region Of Interest manager – My Favourite!
Change a mask (binary image) to a selection (ROI)

## Slide 11: Image Menu
Remember this shortcut
Switch between bit depths and colour type
Many functions in here…
Image meta-data
Dealing with multichannel images
3D images &
time series
Rotate, flip etc
Apply colour to an image

## Slide 12: Selections
Selection tools http://rsbweb.nih.gov/ij/docs/guide/146-10.html#toc-Section-10
Edit menu http://rsbweb.nih.gov/ij/docs/guide/146-27.html#toc-Section-27

## Slide 13: Selection tools
Left click
Right click
for more tools
Double left click
for tool options

## Slide 14: More Selection tools
Good way to edit ROIs

## Slide 15
Editing selection
http://rsbweb.nih.gov/ij/docs/guide/146-27.html#toc-Subsection-27.12
Very useful: it puts your last ROI onto a new image

## Slide 16: Composite selection http://rsbweb.nih.gov/ij/docs/guide/146-10.html#sub:Composite-selections
Add to selection
(release shift key to add non-square selection)
Remove from selection
Selection tool
+
+
File / Open Samples… FluorescentCells.tif
Exercise 6)
Draw a face!

## Slide 17: Magic wand http://rsbweb.nih.gov/ij/docs/guide/146-19.html#toc-Subsection-19.7
Selection range
=
initial value
+/- tolerance
https://imagej.nih.gov/ij/docs/tools.html
Watch this example: (we will do this together in a couple of slides)
Open Sample…
1) Hela Cells 5) Double click the Wand tool
2) Go to channel 3 (Blue) 6) 8-connected.
3) Select a nuclei with the wand… 7) Slide Tolerance…
4) Click in a nuclei

## Slide 18: Overlay http://rsbweb.nih.gov/ij/docs/guide/146-11.html#sub:Overlay-Intro
Image>Overlay
ImageJ/Fiji can create and work with non-destructive overlays.
The overlay is preserved when an image is saved in TIFF format.
Overlay is very useful when using scale bars.

## Slide 19
Highlight one at a time
Rename
Measure (all sorts, covered later)
Properties… (colour, size, width)
Show all
Flatten (careful – Make a duplicate first)
More>> Save as… saves a zip file of all the ROIs
ROI Manager
Add more ‘ROIs’…
Text tool, draw an area, write something, Press T
Arrow tool, press T

## Slide 20
Measurements
Analyze / Set measurements…
Try it…
Open Samples / Hela cells
Use Magic Wand and ROI manager to select each nucleus.
Set a few measurements.
Measure those parameters.
You can save the results window as a excel, .csv or text file
Exercise 7) Measure stuff

## Slide 21: Process. Lots of functions, i.e…
Normalisation: linear stretch of the histogram, but changes the data!
Equalisation: non-linear stretch of the histogram (based on the square root of the intensity see http://homepages.inf.ed.ac.uk/rbf/HIPR2/histeq.htm#1)
Best setting: 0.35% Saturated pixels,
Don’t tick either Normalize or Equalize
Try it, (Images for users / RGB…/ Mito Hela Cells,
(H), (Shift C), Reset Brightness Contrast.
Then Enhance contrast.
Try Find Edges…

## Slide 22
Gamma
Faint objects can be made more intense without saturating bright objects ( <1).
Medium-intensity objects can be made fainter without dimming the bright objects ( > 1).
 = 1
 = 0.5
 = 1.5
Process>Math>Gamma
Built-In function: http://rsbweb.nih.gov/ij/docs/guide/146-29.html#toc-Subsection-29.9
Macro: http://imagej.nih.gov/ij/macros/tools/GammaCorrectionTool.txt
Non-linear, but OK as long as you say what you’ve done.
Do intensity analysis on un-manipulated image tho!
Can be very useful for segmentation.

## Slide 23: Stacks
ImageJ/Fiji can display multiple spatially or temporally related images in a single window
The image set is called a stack and the images that make up a stack are called slices
In stacks, a pixel (which represents 2D image data in a bitmap image) becomes a voxel (volumetric pixel), i.e., an intensity value on a regular grid in a three dimensional space.
All the slices in a stack must be the same size and bit depth.
http://imagej.net/Z-functions

## Slide 24
1
2
Image>Stacks>…
Stack Tools
Plugins
3
Example:
Zebrafish
Z project
Extended Depth of Field

## Slide 25: Stack manipulation (1)
6
1
5
2
3
4
Montage
6
1
5
2
3
4
images
stack
1
2
3
4
5
6
6
5
4
3
2
1
Stack reverser
Sub-stack functions
5
4
3
2
6
5
2
1
Z-projection

## Slide 26: Stack manipulation (2)
6
concatenate
combine
Interleave
De-interleave
Stack inserter

## Slide 27: Image>Hyperstack
Hyperstacks are multidimensional images, extending image stacks to four (4D) or five (5D) dimensions: x (width), y (height), z (slices), c (channels or wavelengths) and t (time frames).
Open sample image ‘Mitosis
2 channels
5 z-slices
51 time-points

## Slide 28
Stack to hyperstack …
Sometimes you get an image series that needs to be put together, for example from Volocity live imaging…
Example: Open samples…mitosis
Image / Hyperstacks / Hyperstack to stack…
Then reverse that with
Image / Hyperstacks / Stack to Hyperstack…
You need to know the stack order, and number in each dimension (xyzct)

## Slide 29: Reduce stack dimensions
Duplicate image (Ctrl+Shift+D)
Individual or all channels
Any range of z slices
Any range of timepoints

## Slide 30: 3D stacks: Examples
Open Samples > Confocal Series
Open Samples > Fly Brain
Open Samples > T1 Head
Try: Plugins / 3D viewer.
Try: Image / Stacks / reslice (shortcut = ‘/’)

## Slide 31: Image Properties (ctrl+shift+P)
Metadata
No Metadata
Image>Properties …
File : Fluorescent cell.lsm
File : FluorescentCells.tif

## Slide 32: Scale Bar
Analyze / Tools / Scale bar… or Analyze / Set Scale

## Slide 33
Image Stitching
Useful for histology (also can do 3D images)
Try it:
Plugins / Stitching / MosaicJ
Open Image Sequence
First image in 2D Stitching folder…
Click each image,
move it to roughly the right place
File / Create mosaic…

## Slide 34
Image Stitching
Lazy way:
Plugins / Stitching / Grid Collection Stitching…
Choose the folder with your files, and wait…

## Slide 35
Image Stitching
Lazy way:
Plugins / Stitching / Grid Collection Stitching…
Works for 3D too…
Use the 3D stitching folder…

## Slide 36
Stack Registration
Plugins / Registration / StackReg (on the BIG-EPFL update site requires ImageScience also)
Translation : basic left right up down - Good basic alignment, little scope for error
Rigid body: rotation also (BEST) - Can make mistakes if segments have big differences.
Scaled rotation: scale also - Can make mistakes if segments have moderate differences.
Affine: most freedom to align - computationally tricky
Plugins /Registration / Linear Stack alignment with SIFT
Implements a patented algorithm assuming the images are all at the same scale.
Rigid is the best.
Useful when you have multiple serial sections
Files: ‘Rat Brain’, ‘H&E’ in Stack alignment folder

## Slide 37
Where is that command?
Press ‘L’ = shortcut to Plugins / Utilities /Find commands
You can search for any command in Fiji...

## Slide 38
Help / Update Fiji
Then Manage update sites…
http://fiji.sc/List_of_update_sites