## Slide 1
Introduction to image processing and analysis with ImageJ / Fiji. Part 3 Digital image processing
Dale Moulding
UCL Institute of Child Health Imaging Facility

## Slide 2: Image processing rules: Dos and Don’ts
Manipulation should be done on a copy not the original data
Simple adjustments to the entire image are usually acceptable
Check journal’s guidances
Ethical guidelines: http://www.ncbi.nlm.nih.gov/pubmed/20567932
Be honest, always describe the adjustments made
Do not hide information (brightness, contrast, level)
Do not create/destroy information (interpolation, bit-depth conversion)
http://jcb.rupress.org/cgi/content/full/166/1/11 JCB article about image manipulation.
http://swehsc.pharmacy.arizona.edu/micro/digital-image-ethics Nice article, picking the best image is not the same as picking the image that fits your hypothesis!

## Slide 3
http://ori.dhhs.gov/education/products/RIandImages/guidelines/list.html
Journals will check your images – they look for noise in the background, smoothing artefacts, replicated images, etc…
Image processing rules: An online guide.

## Slide 4: Background correction
Even background across the image
Image>adjust>Brightness-Contrast
Uneven background
Process>Substract Background (rolling ball algorithm)
Flat field correction (brightfield)
Image Calculator Plus Plugin
Many other ways …
http://imagejdocu.tudor.lu/doku.php?id=howto:working:how_to_correct_background_illumination_in_brightfield_microscopy

## Slide 5: Rolling Ball http://rsbweb.nih.gov/ij/docs/guide/146-29.html#toc-Subsection-29.14
Radius should be set to at least the size of the largest object that is not part of the background
Several iterations may improve the results
Useful to remove white background on gel
Good for Colocalisation
Exercise 1) Rolling ball background correction

## Slide 6: Flat-field correction (Image Calculator Plus Plugin)
Exercise 2) Image Calculator Plus
Average intensity of the flat field image
(this number is wrong, the correct value is found by ‘Analyze / Set Measurements / mean grey value.
Select all (Crtl + A), Measure (M)
i1 : experimental image
i2 : background image
http://rsbweb.nih.gov/ij/plugins/calculator-plus.html (Process / Calculator plus)
i1 : can be a stack, then the background is removed from every image!

## Slide 7: Profile plot (shortcut = K)
http://rsbweb.nih.gov/ij/docs/guide/146-30.html#sub:Plot-Profile-[k]
Displays a two-dimensional graph of the intensities of pixels along a line or rectangular selection.
Remove X and Y gridlines
How to measure dot blots and Westerns…
Method 1: draw a rectangle on first dot press CTRL 1, move to second lane CTRL2, all lanes, CTRL2, last lane CTRL3.
Method 2:

## Slide 8: Measure (shortcut = M)
Saves measurements to Results table
Draw line to define background. (shortcut = D)
Use magic wand to highlight each peak
Measure
Results can be Saved as (File / Save as) and excel file

## Slide 9
How to measure Westerns
Uneven background, lanes very close together, different widths, other bands close by.
Use segmented line tool.
Set the line width to cover the bands.
Plot profile.
Move the line up or down and plot profile of background.
Remove gridlines.
Adjust range.
Use Process / Image Calculator and combine the 2 graphs with ‘min’
Exercise 3) Measure western blot

## Slide 10: Manual Particle counting
ImageJ can facilitate manual counting
      “Cell counter” plugin (Plugins / Analyze / Cell counter)
You click each cell and it gets marked and counted.
Exceedingly dull, slow, but if done carefully very accurate.
Exercise 4) Manual Cell Counter

## Slide 11: Image Segmentation & automatic counting
Automatic image analysis has benefits and pitfalls.
Pros:
Quick
Unbiased
n = lots!
Cons:
Never 100% accurate (but n = lots!)
Time consuming to set up.

## Slide 12: Threshold (shift+T)
46 blobs (excluding edges)
But, are some overlapped?
Are some too small?
Exercise 5) Automatic counting - Threshold

## Slide 13: Threshold (shift+T)
Process /
Binary /
Watershed
(splits over-
lapping blobs)
45 blobs (excluding edges)
Split the overlapped ones
Excluded little ones.

## Slide 14: Spatial filters
http://rsbweb.nih.gov/ij/docs/guide/146-29.html#toc-Subsection-29.11
Smooth
Sharpen
Detect edges
Noise
Filters
Example:
EM filtering, try a few… Median filter keeps edges. Gaussian and Mean smooth edges.
Median
Mean
Gaussian

## Slide 15
What about real samples?
Open file:
Cell counting 1.
Exercise 6) Automatic counting – Real images

## Slide 16
What about real samples?
Try different segmentation algorithms
Image / Adjust / Autothreshold… try all
(or auto local threshold, set it to 20…)
Background correction & median filter then Threshold by Triangle (method 15)

## Slide 17
What about real samples?
Process / Binary / Watershed

## Slide 18
What about real samples?
Alternatively, use Process /Find Maxima
Subtract background (20). Filter / Gaussian (3),
Then find maxima (2, preview, adjust tolerance)
Bingo!

## Slide 19
What about real samples – 2!
Open file:
Cell counting 2
Image / Type 8 bit
Gaussian (3) Filter
then Find Maxima
Try: Maxima Within Tolerance

## Slide 20
What about real samples – 3!
Cilia. Need to know how many and how long they are.
Find maxima no good (only counts them).
Therefore, segment to a binary image then measure the lengths.
How??
Image: Images for users/ Cilia lengths. Choose one image.
Hints:
Background correction. Filter (keeping edges).
Binary Dilate and skeletonize.
Macro: Images for users/ Macros/ Cilia2Dlengths.
Exercise 7)

## Slide 21
Identifying double stained cells
Often you need to measure cells that are positive for a particular stain.
A nuclear or cytoplasmic marker.
Use thresholding to make a binary image of each channel, then use ‘Image Calculator’ to add or subtract images from each other to identify overlaps.
File: Images for users/ Double Stained cells/ Dapi_GreenCytoplasm_RedNuclei.lsm
Procedure:
Dapi: Median(3). Threshold Triangle. Watershed. Analyze particles (20) Masks.
Green: Median(2). Threshold Default.
Analyze paricles (50) Masks.
Red: As for Dapi.
Image Calculator:
Mask C2 AND C3
Combine orig 3 colours + new binary image.
Exercise 8)

## Slide 22
Histology staining analysis:
Colour deconvolution
Image / Color / Color Deconvolution

## Slide 24: Macros http://rsb.info.nih.gov/ij/developer/macro/functions.html
Customisable automation
Written in Macro language
Macro can be recorded
  Try it…
  Files: Gut 7 ki67 circ
  Macros: Ki67_find_maxima_noROI.ijm
  Drag Ki67 maxima macro to imageJ, open first image. Run macro
  Do it manually with Plugins / Macro / record … Create
  Change ‘run’ to ‘doCommand’

## Slide 25
Macros - 2
Can be used to process lots of files, and use any ImageJ function
This example is from ancient fossilized rice grains…
Files: Rice (folder)
Macro: RiceEllipses-CourseVersion.ijm (open the macro – drag to ImageJ)
Need to measure:
Length,
Width,
Area,
Shape descriptors.

## Slide 26
Macros - 3
Or can analyse stacks, here is a scratch assay…
Files: Wound Healing (folder)
Macro: wound_healing.ijm (open the macro – drag to ImageJ)

## Slide 27
Other Examples :
Some imaging outputs your files into individual folders.
Macro: MoveFilesToSingleFolder.ijm
Files: try the ‘Images for Users’ folder
Takes all files from a folder and all subfolders, puts them into a single folder.
If you have a folder full of individual dapi, green, red immunofluorescence images.
Macro: Batch Create 3 colour stack & autocontrast.ijm
Files: Drosophila cells folder
Automate putting 3 colour fluorescent images together.
Sets auto-contrast to fill image histogram for each channel.
Macros – 4: more examples

## Slide 28
Macros – 5: Write a macro to count drosophila nuclei in a folder full of files.
Exercise 9 &10)
Adapt other macros rather than write from scratch.
Use Macro recorder to work out the counting procedure.
Try find maxima, or thresholding.
Try and save the results, perhaps save the summary window at the end.
Try and save an image for each file to see how accurate the counting was.

## Slide 29: Tracking
In Fiji Plugins>Tracking …
      Manual Tracking – Best is MTrackJ
      http://www.imagescience.org/meijering/software/mtrackj/
      http://www.imagescience.org/meijering/software/mtrackj/quickstart/
      MTrack2 (automatic but glitchy)
      TrackMate (can be very accurate – needs practice)
ICY software, very powerful automatic tracking.
Add (start a new track).
Clickety clickety…
Measure
Save.
File: neutrophils.tif

## Slide 30: 3D visualisation
Image>Stacks>3D project …
Volume viewer
http://rsbweb.nih.gov/ij/plugins/volume-viewer.html
ImageJ 3D viewer
      Supports macros
      5D dataset
Open Samples>T1 Head
Open Samples>Fly Brain
Open Samples>Mitosis
Course Images>Zebrafish branchial arches.tif
http://rsbweb.nih.gov/ij/docs/guide/userguide-25.html#toc-Subsection-25.6

## Slide 31: Segmentation plugins
      Statistical region merging
      WEKA Trainable segmentation
      Segmentation editor
      Simple neurite tracer
      SIOX: Simple Interactive object extraction
      3D Objects counter
Stack manipulation plugins
Crop(3D)

## Slide 32
CellProfiler is free open-source software designed to enable biologists without training in computer vision or programming to quantitatively measure phenotypes from thousands of images automatically.
http://www.cellprofiler.org/